## Slide 1: Lecture 2: Computer representation, data classes and Matlab fundamentals
MP574
Jan 24, 2018

## Slide 2: Objectives
How computers work with data
  Number representation and data classes
  Data storage
  Complex number representation
How matlab works
  Create matrices and perform basic operations
  Basic image display

## Slide 3: Number Representation
IEEE-754 standard
Matlab defaults to ‘double’ (double precision floating point)
Most real numbers are not computable
  This would require infinite precision and unlimited memory

## Slide 4: Data Classes
Matlab Syntax
  logical, (u)int8, (u)int16, (u)int32, single, double
C Syntax
  char, char, short, int, float, double
Byte Count (1 Byte = 8 bits)
  1,1, 2, 4, 4, 8
Medical images are often shorts

## Slide 5: Integers
Uint8 range 0 to 255
[1 1 1 1 1 1 1 1]
  27+26+25+24+23+22+21+20=255
[0 0 0 0 0 0 0 1]
  20=1
Int8 range -128 to 127
Two’s complement used when signed

## Slide 6: Two’s Complement
Initial bit can be considered a sign bit, but it isn’t that easy
  0 is positive, 1 is negative
Unsigned:[1 0 0 1]=9
Signed:[1 0 0 1]=-7
Algorithm:[1 0 0 1]
  Complement:[0 1 1 0]
  Add 1:[0 1 1 1]=-7
    Remember minus sign

## Slide 7: Memory Storage (integers)
Big endian vs little endian
Little endian
  Least significant to most significant
  X86 (intel)
Big endian
  Most significant to least significant
  PPC, SPARC, network

## Slide 8: Integer Storage Ambiguities
Using 4 bit atomic size
Unsigned:[1 1 1 1 1 1 1 0]=254
(two’s complement) Signed:[1 1 1 1 1 1 1 0]=-2
Big Endian:[1 1 1 1 1 1 1 0]
  English spoken system
Little Endian:[1 1 1 0 1 1 1 1]
  Reversed byte order
Wraparound at the ends of the storage

## Slide 9: Signed status

## Slide 10: Byte swap

## Slide 11: Why use integers?
Pros
  Small memory and storage
  “Fast” computationally
  Well defined by IEEE
Cons
  Using only integers is very limiting
  Wraparound for mathematical operations

## Slide 12: Single and Double precision
X=(-1)s•(1+f)•2e
  s=sign (1=negative, 0=positive)
  f=mantissa 0≤f<1
  e=exponent (bias 127 or 1023)
Scientific notation
  1.126x103

## Slide 13: Floating point representation
X=(-1)s•(1+f)•2e
  5.126*103 rather than:
    51.26*102 or 0.5126*104
    Is called normalization
Floating point numbers directly represent some integers
http://steve.hollasch.net/cgindex/coding/ieeefloat.html

## Slide 14: Single precision
32 bit (4 bytes)
  1 bit sign
  23 bit mantissa
  8 bit exponent (-127≤e≤128)
  ±~10-44.85 to ~1038.53

## Slide 15: Double precision
64 bit (8 bytes)
  1 bit sign
  52 bit mantissa
  11 bit exponent (-1023≤e≤1024)
  ±~10-323.3 to ~10308.3

## Slide 16: Quick exercises
Bias (offset for exponent) of 4 in these examples
s:[0] f:[0 0 0] e:[0 0 0]
  + 1+0 * 2-4 = 1/16
    Smallest positive number
s:[0] f:[1 1 1] e:[1 1 1]
  + 1+7/8* 23 = 15
    Largest number
s:[0] f:[1 1 0] e:[1 1 1]
  + 1+6/8* 23 = 14
    2nd largest number

## Slide 17: Fundamental Resolution
Machine epsilon (eps)
  Difference between 1 and smallest number >1
S:[0] f:[0 0 0] e:[1 0 0]
  (1+0)=1
S:[0] f:[0 0 1] e:[1 0 0]
  (1+2-3)=1.125
Fundamental resolution of 0.125 for this case

## Slide 18: Floating point number line

## Slide 19: Complex Data
Is really simple, just store 2 numbers, one for the real the other for imaginary

## Slide 20: Matlab Operations
Matlab operates on matricies by default
A=[1 2 3; 4 5 6; 7 8 9];
B=[1 2; 3 4]+i*[4 3; 2 1];

## Slide 21: Matlab Operators
A=[1,2;3,4]
A*A=[7,10;15,22]
A.*A=[1,4;9,16]
A+A=[2,4;6,8]

## Slide 22: Matlab Operators
help '*’
Operators and special characters. Arithmetic operators.
plus - Plus +
uplus - Unary plus +
minus - Minus -
uminus - Unary minus -
mtimes - Matrix multiply *
times - Array multiply .*
mpower - Matrix power ^
power - Array power .^
mldivide - Backslash or left matrix divide \
mrdivide - Slash or right matrix divide /
ldivide - Left array divide .\
rdivide - Right array divide ./
kron - Kronecker tensor product kron

## Slide 23: Image Display
A=magic(128);
figure();
image(A);

## Slide 24: Image Display
A=magic(128);
figure();
imshow(A,[]);

## Slide 25: Image Display
A=magic(128);
figure();
imshow(A);

## Slide 26: Image Display
A=magic(128);
figure();
imagesc(A);

## Slide 27: Image Display
A=magic(128)+i*magic(128);
imagesc(A);
??? Error using ==> image
Error using ==> image
Image CData can not be complex..
  Either use imag(), real(), angle(), or abs() to display components of the image

## Slide 28: Take Home Points
Computers have a finite numerical precision
  Different operations call for differing precision (i.e. Fourier transform operation vs. Image display)
  Except for special math toolboxes
Matlab is a powerful toolbox for matrix operations including image processing
  Idiosyncrasies of image display and complex number representation
  Experiment with image display
  GUI tools on the website: Volume viewer