## Slide 1: Lecture 4 Display Tools: MATLAB, Volume Viewer (MATLAB) and Image J/Fiji David Mummy mummy@wisc.edu
Medical Physics/Biomedical Engineering 574
1022 WIMR, 9:55-10:45 am, MWF Spring 2018

## Slide 2: Outline
Matlab basics
  Brief review of image header concept
  Image i/o basics
  Built-in image display tools in Matlab
  Volume Viewer (custom Matlab GUI)
  Imagescn (custom Matlab toolbox)
ImageJ and Fiji basics

## Slide 3: MATLAB – Does matrix manipulation well

## Slide 4: A BRIEF LIST OF MATLAB COMMANDS
Some Basic Commands (Note command syntax is case-sensitive!)
Commands Useful in Plotting.
matlab loads the program matlab into your workspace.
quit quits matlab, returning you to the operating system.
exit same as quit.
who lists all of the variables in your matlab workspace.
whos list the variables and describes their matrix size.
clear deletes all matrices from active workspace.
clear x deletes the matrix x from active workspace.
... the ellipsis defining a line continuation is three
successive periods.
save saves all the matrices defined in the current
session into the file, matlab.mat.
load loads contents of matlab.mat into current workspace.
save filename saves the contents of workspace into
filename.mat
save filename x y z
saves the matrices x, y and z into the file titled
filename.mat.
load filename loads the contents of filename into current
workspace; the file can be a binary (.mat) file
or an ASCII file.
plot(x,y) creates an Cartesian plot of the vectors x & y.
plot(y) creates a plot of y vs. the numerical values of the
elements in the y-vector.
title('text') places a title at top of graphics plot.
xlabel('text') writes 'text' beneath the x-axis of a plot.
ylabel('text') writes 'text' beside the y-axis of a plot.
text(x,y,'text') writes 'text' at the location (x,y) .
hold on maintains the current plot in the graphics window
while executing subsequent plotting commands.
hold off turns OFF the 'hold on' option.
hist(x) creates a histogram. This differs from the bargraph
in that frequency is plotted on the vertical axis.
mesh(z) creates a surface in xyz space where z is a matrix
of the values of the function z(x,y). z can be
interpreted to be the height of the surface above
some xy reference plane.
surf(z) similar to mesh(z), only surface elements depict
the surface rather than a mesh grid.
contour(z) draws a contour map in xy space of the function
or surface z.
http://www-psych.nmsu.edu/~jkroger/lab/Manuals/MATLAB_commands.htm

## Slide 5: File:Set Path

## Slide 6: A BRIEF LIST OF MATLAB COMMANDS cont.
Data Analysis Commands
max(x) returns the maximum value of the elements in a
vector or if x is a matrix, returns a row vector
whose elements are the maximum values from each
respective column of the matrix.
min (x) returns the minimum of x (see max(x) for details).
mean(x) returns the mean value of the elements of a vector
or if x is a matrix, returns a row vector whose
elements are the mean value of the elements from
each column of the matrix.
median(x) same as mean(x), only returns the median value.
sum(x) returns the sum of the elements of a vector or if x
is a matrix, returns the sum of the elements from
each respective column of the matrix.
prod(x) same as sum(x), only returns the product of
elements.
std(x) returns the standard deviation of the elements of a
vector or if x is a matrix, a row vector whose
elements are the standard deviations of each
column of the matrix.
sort(x) sorts the values in the vector x or the columns of
a matrix and places them in ascending order. Note
that this command will destroy any association that
may exist between the elements in a row of matrix x.
fliplr(x) reverses the order of a vector. If x is a matrix,
this reverse the order of the columns in the matrix.
flipud(x) reverses the order of a matrix in the sense of
exchanging or reversing the order of the matrix
rows. This will not reverse a row vector!
reshape(A,m,n) reshapes the matrix A into an mxn matrix
from element (1,1) working column-wise.
http://www-psych.nmsu.edu/~jkroger/lab/Manuals/MATLAB_commands.htm

## Slide 7: A BRIEF LIST OF MATLAB COMMANDS cont.
SPECIAL MATRICES
ARRAY PRODUCTS
zeros(n) creates an nxn matrix whose elements are zero.
zeros(m,n) creates a m-row, n-column matrix of zeros.
ones(n) creates a n x n square matrix whose elements are 1's
ones(m,n)' creates a mxn matrix whose elements are 1's.
ones(A) creates an m x n matrix of 1's, where m and n are
based on the size of an existing matrix, A.
zeros(A) creates an mxn matrix of 0's, where m and n are
based on the size of the existing matrix, A.
eye(n) creates the nxn identity matrix with 1's on the
diagonal.
length(x) returns the number elements in a vector.
size(x) returns the size m(rows) and n(columns) of matrix x.
rand returns a random number between 0 and 1.
rand(A) returns a matrix of size A of random numbers.
Sometimes it is desired to simply multiply or divide each
element of an matrix by the corresponding element of another
matrix. These are called 'array operations" in 'matlab'. Array or
element-by-element operations are executed when the operator is
preceded by a '.' (period). Thus
a .* b multiplies each element of a by the respective
element of b
a ./ b divides each element of a by the respective element
of b
a .\ b divides each element of b by the respective element
of a
a .^ b raise each element of a by the respective b element
x' The transpose of a matrix is obtained by
interchanging the rows and columns. The 'matlab'
operator that creates the transpose is the single
quotation mark, '.
Miscellaneous Commands
TRANSPOSE OF A MATRIX

## Slide 8: Raw Images vs. Image File Formats
“Raw” images have no header
  Generally a linear array of bytes containing only the signal intensities
Most images (ex. JPEG, TIFF, DICOM) have extra data stored in the header
  Image data structure and size
  Image compression encoding
  Acquisition parameters
  Patient information (PHI – protected health information)
…more in Lecture 6
raw image file
image file
header
image data
image data

## Slide 9: Image Header Example
http://www.sph.sc.edu/comd/rorden/dicom.html#header
*Digital Imaging and Communications in Medicine (DICOM)

## Slide 10: Image Processing Tools in MATLAB
Import
Export
Get image information
View images
  imshow
  imagesc
  volumeviewer
  imagescn

## Slide 11: Import/Export MAT data (Example 1)

## Slide 12: Import/Export raw data (Example 2)

## Slide 13: Import/Export image files (Example 3)

## Slide 14: Image Info (Example 1-3)
For image files, use MATLAB function imfinfo displays info without reading into workspace (reads the header)
  imfinfo(‘name.jpg’)
For dicom files, use MATLAB function dicominfo displays info without reading into workspace (reads the header)
  dicominfo(‘name.dcm’)
Read image into workspace (see previous slides)
Once image is read into workspace
  ‘whos’ sees information about the data in your workspace
  ‘size(X)’ gives you the size of variable X
  ‘max(X)’ gives max value of 1D array X
  ‘max(max(X))’ or ‘max(X(:))’ gives max value of 2D array X

## Slide 15: Image Processing Tools in MATLAB
Import
Export
Get image information
View images
  imshow (Matlab)
  imagesc (Matlab)
  volumeviewer (custom GUI)
  imagescn (custom toolbox)

## Slide 16: Image Processing Tools in MATLAB
http://www.mathworks.com/help/toolbox/images/ref/f3-23960.html
LOTS OF FUNCTIONS!
Don’t waste time doing it yourself, there’s probably a function that does it for you!
However, they might not be perfect….performance, efficiency, etc
  example: imshow scales image from 0 to 1, might not be desirable
Good to know how they work
Use ‘Help’ in Matlab, it’s wonderful documentation on how the functions work.

## Slide 17: imread() and imfinfo()
(saw some of these already)
  % reads in images of most filetypes
  % Data concerning image size, compression, colormap read from the header
  % data are 8 bit unsigned but note the 3 color channels, red, green, blue.

## Slide 18: imwrite()
Can generate different image formats automatically

## Slide 19: Consider compression ratios…
JPG
BMP
TIFF
Calculated Matrix Size
= 732 X 486 X 3 bytes = 1.07 MB

## Slide 20: Display Tools in Matlab

## Slide 21: imagescn toolbox
Developed by NIH, but not supported
W/L
ROI
Distance
Movies
Point Measure
Image Rotation
Crop
imagesc tools

## Slide 22: imagescn: Easy to Use Basic ROI Tools

## Slide 23: All of these examples can be replicated line by line (Matlab R2016a) Tutorial for Volume Viewer and Image J on Learn@UW

## Slide 24: Load into the workspace a single dicom image:
% load in a single image if the brain using dicomread %
brain2 = dicomread('brain__5’);
% Alternatively if you reshape brain_bin %
brain3 = reshape(brain_bin,128, 128, 36);
% one can then load in the matrix as a time series in volume viewer as a matrix, for example: %
brain3(:, : , :)
% This is a time series of contrast perfusion in the brain %

## Slide 25: Volume Viewer: Matlab GUI
Developed by Dr. Rafael O’Halloran

## Slide 26: ImageJ/Fiji (http://fiji.sc/): Stand Alone Windows/Mac Program from NIH
Functionality
Window and Level
ROI measurement
ROI measurement through image series
Plot line profile
Play as a movie
Rotate & Zoom images
Mathematical operations on images
Apply filters
Fourier Transform
And the list goes on….
Unique from the rest of this presentation b/c it’s NOT Matlab based

## Slide 27: Assignment
  ImageJ/Fiji, volumeviewer, and imagescn
  See tutorial for ImageJ/Fiji and volumeviewer on Learn@UW
  “Brain” image data set: 2D dynamic perfusion MR images
    imginfo text file describes file size and data types
    brain binary file on Learn@UW
  Links to software sites online:
      https://www.slicer.org
      https://imagej.net/Welcome
      http://www.itksnap.org/pmwiki/pmwiki.php